## Slide 1
Fountain Spectrometer
Alexander Koukras
Gyula Nagy
Miguel Fernández

## Slide 2: Topics
Geometry
Calibration
Transmission
Focusing properties
Resolution
Conclusions

## Slide 3: Geometry
Just PPA with 2π cylindrical symmetry (rotating around x axis)
Advantage compared to PPA:
  Greater acceptance: more solid angle (2π symmetry)

## Slide 4: Calibration
Linear relation between E0 and Vd
Here, q=-1 (e) so
For 45º
Relation Vd, E0 :
Using LUA

## Slide 5: Calibration (45º & 30º)
Slope 
Formula 
Chart: KE vs V 45º
Chart: KE vs V 30º
Slope 

## Slide 6: Transmission
T(%) =
For a fixed KE of particles and its corresponding Vd (calibration)
Fly particles slightly different angles 
measure #particles enter, #particles pass through
45º  T= 98.5%
30º  T= 20% !!!
Wider exit slit + 3rd plate (only for 30º)

## Slide 7
Transmission (3 plates)
Now: T = 92%
f does not change
3rd plate not to lose resolution

## Slide 8
For 45º  1st order focusing, focus inside
For 30º  2nd order focusing, focus outside
Trace width:
Focusing properties
 | Simion | Theoretical
30º | 0.2 | 0.03
45º | 2 | 1.3

## Slide 9: Resolution
Lua program to scan energy, measure the Emin and Emax that leave the exit slit, and calculate R
  The lower R  the better
 | R
45 º | 1.8 %
30 º | 1%

## Slide 10: Resolution
Compare 45º with theory:
 | Simion | Formula
45° | 1.8% | 3%

## Slide 11: Resolution
Independent of energy
30º has better resolution for same geometry
For 30º, R does not change with 3rd plate + wider exit slit

## Slide 12: Conclusions
Better resolution for 30º
Better focusing for 30º
Lower transmission for 30º
  Solution: 3rd electrode + wider exit slit

## Slide 13: All information
QR Code
fountainspectrometer.blogspot.com

## Slide 14
Thanks to our advisors:
  Manolis Benis
  Pilar Garcés
  And all other CPOTS teachers
Thanks for your attention